## Slide 1
Improving DSD9’s Performance
Goal to bump up the clock rate (to 75MHz (13.3ns)).
Starting worst timing about 21 ns. (approx 47MHz fmax)
Improved timing to 17.5 ns. (approx 57 MHz fmax)
Worst path is for state transitions
First Item on Critical Path:
  The Floating Point Unit.
Simple solution: remove it. (shaves 2ns off of clock)
Next solution-> use a lower speed clock for the FPU, and a higher
Clock rate for the CPU.

## Slide 2
Next two items on critical path:
  PC incrementing
  Loading of R1,R2 for local exception handling.
PC increment timing can be improved by placing restriction on the amount the
PC increments by, and adding additional pipelining in the IFETCH stage.
-> moved off the critical path with these changes
Loading of R1,R2 for local exception handling can be handled by simply eliminating
It, thus making the core smaller as well.
Next item on critical path:
  State register
The state register timing can be improved by reducing the number of state
Transitions. This can be done by reorganizing the code to be more efficient.
State transitions that can be hoisted upwards outside of control flows will improve
Timing. Reorganizing the code shave 2ns off the timing.
Next item on critical path:
  “B” operand register

## Slide 3
Next item on critical path:
  ALU
The ALU can’t be optimized much more than it is already.
-> floorplanning may help
Adding additional registers into the ALU path would not likely increase performance
Because it would turn ALU operations into multi-cycle ones. The clock frequency
May increase but so does the CPI.
-> the only other thing is to remove some of the ALU’s features.

## Slide 4
Logic
Shift
Mul / DIV
Add / Sub
Bitfield
MEM
Loads
CSR
A
B
I
FWD_MUX
Operand registers feed the ALU,
The ALU output then travels through
A forwarding multiplexer back to the operand
Registers.
Unfortunately when this becomes the
Critical path there isn’t much that can
Be done about it. The ALU outputs can’t be registered
Because that would add a clock cycle to every ALU operation
Cutting the performance of the core in half.
Only a couple of options:
Reduce the number of supported operations.
Floorplan manually.

## Slide 5
ICache
oreg
PC inc.
Inst. AlignMux
IR
IRQ Mux
Ext. IRQ
Int. IRQ
Decode reg / branch /
PC Inc
DSD9 – Previous IFETCH Stage
Decode / Register Fetch Stage
Inv. Clk
The previous design of the IFETCH stage decoded the output of the Icache directly
Without the register for instruction alignment. This was made possible by using an inverted
Clock to register the cache output. Inverting the clock however means that there is only
½ of a clock cycle available for decoding. Consequently the design runs at a substantially
Lower fmax.
The decode from the cache through to the PC incrementer and back to the cache again was 20 logic levels and on the critical timing path. Optimizing
This path by simplifying the decodes substantially improved performance, bu the basic design isn’t high performance due to the lack of registers pipelining.
This design does support high code density because variable length instructions can be used.

## Slide 6
ICache
oreg
PC inc.
Inst. AlignMux
oreg
IR
IRQ Mux
Ext. IRQ
Int. IRQ
The PC incrementer can’t use the result of the decoded instruction (size) because
That’s three clock cycles after the cache is accessed. There would be a three cycle delay
For every instruction in which case a non-overlapped pipeline might as well be used.
Given that the PC increment can’t use decodes it has to be by a fixed amount, it can’t vary. The cost is code density.
Decoding the Icache directly isn’t possible for performance reasons. There is now a full clock cycle for decoding.
The instruction alignment mux selects an instruction from cache lines and shifts it into position for subsequent decoding. The output of this mux is registered because it’s likely three or more logic levels by itslef.
The IRQ mux is present to allow the core to handle interrupts which must be forced into the instruction stream. Some simple decoding for the register selects and possibly branch prediction are performed here in order to save a clock cycle over using the IR decode stage.
Because the pipeline is longer than the previous version branches require more clock cycles to execute (5). Since this represents 20% of instructions affected by 25%, ( double the clock cycles but only for taken branches) the performance loss (for a higher fmax) is about 5% overall.
Branch prediction isn’t as helpful because it has to be done on decoded instructions, costing two clock cycles.
Decode reg / branch
DSD9 – IFETCH Stage (newer)
Decode / Register Fetch Stage

## Slide 7
Branch Prediction:
Because it’s three clock cycles before the branch can be decoded, correctly
Predicted branches that are taken take three clock cycles. Correctly predicted branches that are not taken require only a single clock cycle. Incorrectly predicted branches require five clock cycles because
It isn’t known until the execute stage that the branch was incorrectly predicted.
Single cycle not taken branches are relatively the same as not taken branches without branch prediction present. So with branch prediction sometimes taken branches require 3 clock cycles, and sometimes 5. This isn’t bunches better than without any branch prediction at all. Removing the branch predict logic would make the core smaller and possibly increase the fmax. It might be better to
Have a smaller core without branch prediction.

## Slide 8
Logic functions represent a kind of minimum to the amount of logic required to do something useful. Each bit processed is independent
Of the other bits and there is no cascade of logic cells required. There is little point in having these operations spread across multiple
clock cycles to try and improve performance.
Logic functions are decoded in the EX stage. There isn’t a lot of benefit to decoding the functions in the decode DC stage and passing the
Decodes forwards. To do it that way the problem is that there would be *more* signals to process and use in the multiplexer required to
Determine which operation output to use. It would require a case statement with eight or nine inputs anyways.
The fewer signals passed around the core the better. Signals require routing and make core larger.